Chapter 11

Th e process of camera calibration gives us both a model of the camera’s geometry and a distortion model of the lens. Th ese two informational models define the intrinsic parameters of the camera.

1.Mathematically remove radial and tangential lens distortion; this is called undistortion and is detailed in Chapter 11. Th e outputs of this step are undistorted images.
2. Adjust for the angles and distances between cameras, a process called rectifi cation.
Th e outputs of this step are images that are row-aligned† and rectifi ed.
3. Find the same features in the left and right ‡ camera views, a process known as cor-respondence. Th e output of this step is a disparity map, where the disparities are the differences in x-coordinates on the image planes of the same feature viewed in the
left and right cameras: x l – x r .
4. If we know the geometric arrangement of the cameras, then we can turn the dis-
parity map into distances by triangulation. Th is step is called reprojection, and the
output is a depth map.

Stereo calibration is the process of computing the geometrical relationship between the two cameras in space.

Stereo calibration depends on finding the rotation matrix R and translation vector T
between the two cameras, as depicted in Figure 12-9. Both R and T are calculated by the
function cvStereoCalibrate()

the rotation matrix will put the right camera in the same plane as the left camera; this makes the two image planes coplanar but not row-aligned (we’ll see how row-alignment is accomplished in the Stereo Rectification section below)

stereo rectification is the process of “correcting” the individual images so that they appear as if they had been taken by two cameras with row-aligned image planes (review Figures 12-4 and 12-7).